|  | ......................... Pc. .............................. € .............................. € Revolving door system in three or four-leaf design with freely selectable interior diameter up to 3800 mm 75 mm canopy height Drive fully integrated into the ceiling construction TÜV type-tested according to DIN EN 16005 Visible width of drum profile 60 mm Drive types ( ) Manual operation of the door. or ( ) Manually operated door with speed limiter or ( ) Manually operated door with positioning device or ( ) Fully automatic revolving door system (activated via movement detector) Power supply: 230 V / 50 Hz / 330 W / 10 A, programme switch for adjusting the mode of operation. Connection to the building management technology with preset inputs and outputs possible. Tested in accordance with DIN EN 16005:2013-01 Construction dimensions: ( ) Outside diameter: ..................mm (freely selectable between 1880 and 3880 mm) ( ) Clear passage height DH: .... .. mm (up to 3500 mm, higher on request) ( ) Total height of door system: ...............mm ( ) Floor recess: ................ ..........mm (min. 60 mm) Note: Installation distance 40 mm on all sides Door position in façade: ( ) central ( ) off-centre, offset: …..mm Model type: ( ) three-leaf ( ) four leaf Side-hung leaf: Fixed door leaves, fine-framed, 65 mm visible width to mount toughened safety glass. Drum walls fine-framed on 3 sides using aluminium profiles with 60 mm visible width. Side panel joint with integrated hollow chamber for cable guidance up and/or down. Side panel filling with: ( ) Curved LSG 10/12 mm, clear or ( ) Curved thermally insulated panel filling 22 mm thick or ( ) Smooth-surface offset thermally insulated panels approx. 34 mm thick Aluminium ceiling construction: ( ) 75 mm standard height ( ) ___ mm with elevated ceiling construction (200 – 1200 mm) Roof covering outside: ( ) Visible sheet metal covering made of 2 mm aluminium in system colour or ( ) Waterproof roof with 2 waterspouts (flat roof without incline) Roof covering inside: Visible sheet metal covering made of 2 mm aluminium in system colour Soffit: ( ) Consisting of aluminium circle elements in system colour incl. inspection opening Surface of the light alloy parts: ( ) Powder coating according to RAL or ( ) LM anodised E6/EV1 or ( ) Colour anodised ............ or ( ) Coated with ground stainless steel, grain 240 (1.4301) or ( ) Coated with polished stainless steel (1.4301) Floor ring ( ) Floor ring made of rectangular tube 30x30x2 mm, stainless steel, also serves as the border for the floor covering. ( ) Sheet metal base from 100 mm and/or ( ) Loose fixed flange according to DIN 18533 or ( ) Direct installation of the self-supporting drum construction to the top edge of the finished floor. Note: Only possible with sufficient load-bearing and flat finished floor level.(+/- 1mm) Note: Building sealing is an external service. Floor covering ( ) Entrance mat, anthracite colour, 22 mm high, more colours available on request! or ( ) Without floor covering Delivery and installation Wiring to be carried out on site according to the specifications by an electrical contractor. Installation, commissioning and instruction of the operator as well as documentation handover in accordance with / EN 16005 / DIN 18650 by plant fitters or service partner. |
| --- | --- |
|  | ......................... Pc. .............................. € .............................. € Night-time closer with continuous 4-point guide (optional position) ( ) Night-time closer sliding doors externally guided, manual, lock possible from inside and outside. ( ) fine-framed in LSG 10/12 mm, clear or ( ) with aluminium panels Locking of the night-time closer sliding doors using: ( ) Hook bolt lock (no lock monitoring possible, 3-point guide) or ( ) Bar lock at top Locking monitoring (bolt contact possible) ( ) Night-time closer sliding doors internally guided, manual, lock possible from inside and outside. or ( ) Night-time closer sliding doors automatic, internally guided, with deadman control and battery pack for emergency opening in case of a power failure. ( ) With toothed belt locking ( ) With automatic rod locking or ( ) Night-time closer sliding doors automatic, internally guided, with activation via the building management technology and battery pack for emergency opening in case of a power failure. ( ) With toothed belt locking ( ) With automatic rod locking Optionally available: ( ) End position monitoring for night-time closer sliding doors ( ) Bolt monitoring for night-time closer sliding doors |
|  | ......................... Pc. .............................. € .............................. € Locking (optional position) ( ) Without locking mechanism or ( ) Manual locking with extended bolt lock integrated into the door leaf, including Euro profile half cylinder or ( ) Electro-mechanical two-stage locking |
|  | ......................... Pc. .............................. € .............................. € Handles (optional position) ( ) Polished, horizontal stainless steel pull handles, diameter 30 mm, installation directly on the glass, length: ….. or ( ) Polished, vertical stainless steel pull handles, diameter 30 mm, installation directly on the glass, standard length up to 1500 mm ( ) Polished, vertical stainless steel pull handles, diameter 40 mm, installation directly on the glass, length according to the door leaf height |
|  | ......................... Pc. .............................. € .............................. € Operation (optional position) Key switch to “lock” the programme switch to prevent unauthorised changing of the mode of operation, IP rating IP 40 ( ) Surface-mounted ( ) Flush-mounted |
|  | ......................... Pc. .............................. € .............................. € Push pad (optional position) ( ) Delivery and installation of two push buttons with wheelchair symbol on the right post of the revolving door. When these buttons are pushed, the revolving speed is reduced in order to offer more safety to persons with physical restrictions. |
|  | ......................... Pc. .............................. € .............................. € Lighting (optional position) ( ) ..... piece LED spotlight (max. 2.6 W per light) integrated in the soffit or ( ) ..... piece recess for lighting to be installed on site (diameter = ..... mm) |
|  | ......................... Pc. .............................. € .............................. € Hot-air curtain system (optional position) ( ) Hot-air curtain system fully integrated into the ceiling construction of the revolving doors, incl. exhaust tunnel in the canopy area. Operated using a control panel. Connection to the building management technology is possible. The minimum canopy height depends on the diameter. Hot-air curtain system design with: ( ) Electric connection: Heat output: ............KW/ airflow: .............m³/h ( ) Hot water connection Heat output: ............KW/ airflow: .............m³/h Note: We recommend consulting with a specialist planner to dimension and specify the air curtain. It will be connected to the heating system on site. |
|  | ......................... Pc. .............................. € .............................. € Façade connection ( ) Side U profile with connection panels on all sides, 34 mm in system colour from GEZE incl. installation and sealing. |