|  | ......................... pcs. .............................. € .............................. € GEZE Slimline fanlight opener OL 320 with opening width 320 mm, for 1 vertically installed bottom-hung casement, inward opening, with electric drive E 212 R, 230 V AC, for group actuation via several operating spots, scissors with safety button, rod covered with aluminium profile, Motor installation: ( ) vertical at the left-hand side ( ) vertical at the right-hand side ( ) horizontal at the top Leaf width: ........ mm With vertical motor installation ( ) 1 scissors for casement widths from 680 - 1200 mm1) ( ) 2 scissors for casement widths from 1201 - 2400 mm1) ( ) 3 scissors for casement widths from 2401 - 3600 mm1) With horizontal motor installation ( ) 1 scissors for casement widths from 890 - 1200 mm1) ( ) 2 scissors for casement widths from 1201 - 2400 mm1) ( ) 3 scissors for casement widths from 2401 - 3600 mm1) Casement height: ........ mm (min. 530 mm with vertical motor installation) (min. 400 mm with horizontal motor installation) Space required at the side: ........ mm (min. 35 mm with vertical motor installation) Space required at the top: ........ mm (min. 36 mm with horizontal motor installation) Colour: ( ) silver-coloured ( ) white 9016 ( ) RAL ........ 1) Heed panel widths Note: When fanlight opening systems are used on bottom-hung casements, we prescribe the use of separate safety scissors for product liability reasons. These represent an additional safety feature which guarantees the permanent connection fo casement and frame, e.g. GEZE FPS |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE FPS gripping and cleaning scissors ( ) Size 1 from casement height 360 mm ( ) Size 2 from casement height 540 mm ( ) Size 3 from casement height 740 mm |
|  | ......................... pcs. .............................. € .............................. € “Open-Stop-Close” push button control, ( ) LTA-230, mounted flush to wall ( ) Optional: box for surface mounting |