|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer TS 5000 with mechanical hold-open device, with guide rail, hold-open bracket with precise variable adjustment between 80° and 130°, hold-open position can be overridden, closing force in accordance with EN 1154, closing speed, back check and latching are front adjustable, with visual closing force display, standard installation on door leaf/hinge side ( ) TS 5000 closer body size EN 2-6, up to leaf width 1400 mm ( ) TS 5000 ECline closer body, size EN 3-5, with very high efficiency > 80% for barrier-free doors in accordance with DIN 18040, up to leaf width 1250 mm ( ) TS 5000 SoftClose closer body, size EN 2-6, up to leaf width 1,400 mm, for barrier-free doors in accordance with DIN 18040, up to leaf width 1,100 mm, quiet and safe closing even in changing pressure conditions, with one valve integrated in the closer body for the gradual adjustment of the end closing speed for braking or accelerating the door between 15° and 0° ( ) TS 5000 L SoftClose closer body, size EN 3-6, adjustment of the latching action speed to decelerate or accelerate the door between 15° and 0°, up to leaf width 1400 mm Alternative to the guide rail with hold-open device: ( ) with T-Stop guide rail, with integrated opening restrictor and mechanical hold-open device Colour: ( ) silver-coloured ( ) dark bronze ( ) white ( ) stainless steel optic ( ) acc. to RAL Note: Not approved for use on fire protection doors! |
| --- | --- |